## Slide 1: Strategic Defense of Feedback-Controlled Parallel Servers against Reliability and Security Failures
Qian Xie
qianxie@nyu.edu
qx66@cornell.edu

## Slide 2: Outline
Introduction
  Motivation: security risks in network systems
  Example: dynamic routing in ITSs
  Research questions
Model formulation
  Queueing model
  Reliability failures: Markov decision process
  Security failures: attacker-defender game
Results
  Stability criteria
  Optimality results
  Numerical study
  Equilibria analysis
Conclusion
Notes: The presentation will proceed as follows. First, I will give an introduction on security risks in network systems. I will also show you an illustrating example of dynamic routing in intelligent transportation systems. Following this, several interesting research questions around this topic are raised. Next, I will present our queuing model, decision model and game model, then move on to the discussion of our main results. Last, I will summarize our key findings.

## Slide 3: Motivation: security risks in network systems
Network systems rely on data collection and transmission
  Intelligent transportation systems (ITSs)
  Manufacturing systems (production lines)
  Communication networks
Cyber components susceptible to data loss and data errors
  E.g., traffic sensors and traffic lights can be intruded and manipulated
  Need secure-by-design features
Notes: Network systems rely on data collection and data transmission. However, the lack of secure-by-design features makes them susceptible to data loss and data errors. For example, in intelligent transportation systems, researchers have found that traffic sensors and traffic lights can be easily intruded and manipulated. Also, news reported that an artist used 99 phones to fake a traffic jam on Google Maps. We can expect that in the near future, hackers may spoof traffic sensor data or create phantom traffic jams in navigation apps for selfish or malicious intent (e.g., leading other vehicles to take a different road). Similar security risks also exist in manufacturing systems and communication networks.

## Slide 4: Example: dynamic routing in ITSs
Notes: This is a simple example to illustrate the security risks lying in intelligent transportation systems. Consider parallel roads from an origin to a destination. The system operator routes each arriving vehicle to one of the links according to real-time traffic condition. However, such observations can be attacked by some malicious adversaries and the system operator has resources to secure or recover the observations. The resources may be limited or costly, so the system operator has to make careful decisions.

## Slide 5: Research questions
Modeling & analysis
How to model stochastic & recurrent faults/attacks?
How to quantify attacker’s incentive?
How to quantify the impact due to faults/attacks?
How to evaluate various security risks?
Resource allocation
How to allocate limited/costly security resources, including redundant components, diagnosis mechanisms, etc.?
Decision making
How to make protecting (resp. defending) decisions in the face of random faults (resp. malicious attacks)?
Notes: Now, to address such issues, we develop the following research questions. How to … As far as we know, they have not been well studied in conjunction with the dynamics of the network systems, which is typically modeled as queuing processes.

## Slide 6: Parallel-queueing system
Basic model
Poisson arrivals of rate
Parallel servers with service rate
State: vector of queue lengths
Dynamic routing: dynamically allocate jobs (e.g., customers, vehicles, components, data packets) to servers
Provably optimal routing policy: join-the-shortest-queue (JSQ)[1]
Existing works based on perfect observation of system state and perfect implementation of dynamic routing
Faulty/failed closed-loop can be worse than open-loop (e.g., round robin or Bernoulli routing)
Research gap: designing fault-tolerant dynamic routing
[1] Ephremides, Anthony, P. Varaiya, and Jean Walrand. "A simple dynamic routing problem." IEEE transactions on Automatic Control 25.4 (1980): 690-693.
Notes: To start from scratch, we consider a parallel queuing system with Poisson arrivals and symmetric servers. We are specifically interested in dynamic routing with security risks. The idea of dynamic routing is dynamically allocating jobs to servers. Jobs can be vehicles in transportation system, components on production lines and data packets in computer networks. It has been proved that without failures, the send-to-shortest-queue policy is optimal if the system operator has perfect observation of the system state, i.e. the vector of queue lengths and perfect implementation of the dynamic routing. However, if the observation is imperfect, there is chance that the send-to-shortest-queue policy is even worse than open-loop routing policies such as Bernoulli routing policy.

## Slide 7: Protection against reliability failures
Reliability failures
  Random malfunction: fault occurs with constant probability
  Operator loses observation of the states or fails to send instructions
Markov decision process
  Operator protects the routing with state-dependent probability
  Minimize expected cumulative discounted queuing cost + tech cost
Notes: In this work, we consider two types of failure modes. The first one is the reliability failures, say random malfunction that makes the jobs fail to receive routing instructions from the system operator and the DoS attack that cuts off the system operator’s observation. With constant probability , a job joins a random queue, with equal or nonequal probabilities.
We model the system operator’s decision-making problem as a Markov decision process. For each arrival, the operator protects the routing with state-dependent probability . Following the protected routing, a job can definitely be allocated to the shortest queue.
Technological costs including human labor and investments in software/hardware
In this work, we consider two types of failure modes. The first one is the reliability failures, say random malfunction that makes the jobs fail to receive routing instructions from the system operator and the DoS attack that cuts off the system operator’s observation. With constant probability 𝑎, a job joins a random queue, with equal or nonequal probabilities.
We model the system operator’s decision-making problem as a Markov decision process. For each arrival, the operator protects the routing with state-dependent probability 𝛽(𝑥). Following the protected routing, a job can definitely be allocated to the shortest queue.
Technological costs including human labor and investments in software/hardware

## Slide 8: Defense against security failures
Security failures
  Denial-of-service (DoS): operator loses observation temporarily
  Spoofing: attacker compromise sensing (e.g., send-to-longest-queue)
Stochastic attacker-defender game (attacker side)
  Manipulate the routing with state-dependent probability
  Maximize expected cumulative discounted reward
Notes: The second one is the security failures, say the spoofing that can manipulate the system operator’s observation or instruction. Now we formulate the interaction between the attacker and the system operator as a stochastic attacker-defender game.

## Slide 9: Defense against strategic attacks (cont’d)
Security failures
  Routing fails iff attacked and not defended (i.e., & )
Stochastic attacker-defender game (operator side)
  Defend the routing with state-dependent probability
  Minimize expected cumulative discounted loss

## Slide 10: Stability criteria
Theorem 1. The parallel n-queue system with reliability failures is stable if for any non-diagonal vector ,
Theorem 2. The parallel n-queue system with security failures is stable if for any non-diagonal vector ,
Proof sketch. Consider the quadratic Lyapunov function and apply the infinitesimal generator.
Notes: We know that without failures, a n-queue system is stable if and only if the demand is less than the total capacity, i.e. λ < nµ. However, even this condition is satisfied, reliability and security failures can still destabilize the queuing system. Therefore, we have to add more conditions to the stability criteria.

## Slide 11: Stability criteria (cont’d)
Theorem 1. The parallel n-queue system with reliability failures is stable if for any non-diagonal vector ,
Characterization of the threshold:
Notes: For example, under this set of parameter, when observing queue lengths as in the shadow area, if the system operator not protects, then the system can be destabilized.

## Slide 12: Optimal protecting policy
Theorem 3. Consider a parallel n-queue system with reliability failures. The optimal protecting policy is threshold-based.
  Bang-bang control: operator either protects or does not protect (no probabilistic protection), i.e.
  Operator is more likely to protect when 1) the queue lengths are less ‘‘balanced’’; (2) the queues are close to empty
Proof idea: HJB equation and induction on value iteration.

## Slide 13: Stability-constrained optimal policy

## Slide 14: Numerical study
The incentive to protect is non-decreasing in the failure probability , non-decreasing in the tech cost , and non-decreasing in the throughput (estimation of the optimal protecting policy is based on the truncated policy iteration).
Tipping points of the operator starting to protect

## Slide 15: Numerical study (cont’d)
Simulation result: the optimal closed-loop protecting policy performs better in terms of the cumulative cost, compared to the open-loop policies (benchmark) never defend and always defend.

## Slide 16: Attacker-defender game
Definition. The equilibrium Markovian attacking (resp. defending) strategy (resp. ) satisfies that for any state ,
,
.
Attacker’s (resp. defender’s) is (resp. ). In particular, is a Markovian perfect equilibrium (MPE).
Remark. According to Shapley’s extension on minimax theorem,
Proof idea. Induction on value iteration.
Question. Existence of MPE? - Countable infinite state space!
Question. Estimation of MPE? - Adapted Shapley’s algorithm.

## Slide 17: MPE analysis
Theorem 4. The MPE has the following regimes depending on and
  (low risk)
  (medium risk)
  (high risk)
The equilibrium strategies and are both threshold-based.
Notes: As for the regimes of the Markovian perfect equilibria, there are three cases depending on the technological costs: (0,0), (1,0) and somewhere in the middle.

## Slide 18: MPE analysis (cont’d)
Theorem 4. The MPE has the following regimes depending on and
  (low risk)
  (medium risk)
  (high risk)
The equilibrium strategies and are both threshold-based.

## Slide 19: Conclusion
Without secure dynamic routing, random faults and malicious attacks can destabilize the queueing system
The optimal protecting strategy and the equilibrium of attacker-defender game have threshold-properties
The system operator has higher incentive to protect when
  the failure probability is higher
  the tech cost is lower
  the throughput is higher
  the queue lengths are less ‘‘balanced’’
  the queues are close to empty
Our proposed optimal protecting policy (closed-loop) performs better than the benchmark (open-loop)
Optimal protecting strategy (resp. equilibrium) can be estimated by truncated policy iteration (resp. adapted Shapley’s algorithm)